## Slide 1: PDM Microphone Interface with BLE

## Slide 2: PDM Microphone in Remote Control
  All-Digital, Lowest BOM solution
  High quality audio decimation for PDM microphones
  Active Power (measured): 5mA* @ 24MHz CPU operation
  Only 12% CPU utilization for PDM microphones processing (16-bit/16kHz) at 24MHz operation
  Microphone interface up to 24-bit/48kHz configuration
  Optional Trackpad, Motion Sensor and Proximity Gesture features
  UDB = Universal Digital Block (PLD)
PSoC 4 BLE
BLE
CapSense
Digital MEMS Microphone
(Direct PDM Input)
Cortex M0 MCU
5th order CIC Integrator (UDB)
Microphone Sampling Clock Generator
(Fractional Divider)
PDM
Clock
MEMS PDM Interface
Optional
I2C
Trackpad
Motion
Sensor
PDM
Data
5th order CIC Comb
DC Filter
ADPCM
BLE Scheduler
Voice over BLE
  *5mA is PDM only current. BLE + PDM + DC filter + ADPCM power consumption is of the order of 11-12mA (non-optimized number)

## Slide 3: PSoC 4 BLE PDM Solution
Two-wire mic connection, no external components required
5th Order hybrid CIC filter implementation
    5th Order Integrator is realized using 4 hardware UDBs*
    5th Order Comb, DC filter, and ADPCM (4:1) are implemented in firmware
    32-bit datapath for CIC, end result is truncated to 16-bit for ADPCM or similar compression schemes
Minimal firmware (<700 bytes flash & <50 bytes SRAM) & low CPU intervention (<12% CPU usage)
Tested at 24MHz system operation, can go as low as 12MHz (not tested yet)
Additional peripherals (ADC, OpAmp, Comparator, Communication blocks, TCPWMs**, and other PSoC Components) for system integration
CIC droop correction is NOT part of the design
  Optional
  *UDB = Universal Digital Block **TCPWM = Timer/Counter/PWM block
Digital MEMS Microphone
(Direct PDM Input)
Cortex M0 MCU
5th order CIC Integrator (UDB)
Microphone Sampling Clock Generator
(Fractional Divider)
PDM
Clock
MEMS PDM Interface
PDM
Data
5th order CIC Comb
DC Filter
ADPCM
PSoC 4 BLE
Notes: question: any potential interest in stereo operation? That should be possible, with some small compromises.

## Slide 4: PDM Voice Performance**
  Average THD+N of >-70dB until Fs/3*
  *Measured using Industry standard Prism Dscope equipment with CT detector band pass filter of 22Hz to 8kHz
  **Measurement Setup = Prism Analog Signal Generator-> PDM OUT -> PDM block in PSoC 4 BLE -> I2S OUT -> 24-bit Audio DAC -> Prism Analog Signal Analyzer
  No spurious sidebands
  Amplitude Vs. THD+N
  Input Vs. Output
  Sample
  Recording

## Slide 5: ADPCM over BLE Voice Performance*
  *Applies 4:1 ADPCM compression scheme at the output of PDM samples
  1K Tone Frequency Response
  Amplitude Vs. THD+N
  Input Vs. Output
  Frequency Vs. THD+N

## Slide 6: CPU Utilization
  PDM + 4:1 ADPCM Only
  *System clock set to 24MHz
  PDM Only
  PDM, ADPCM & DC Filter
Mode | CPU Utilization* %
PDM only | 12% (7.7us every 62.5us)
PDM & ADPCM | 33% (20.7us every 62.5us)
PDM, ADPCM, & DC Filter | 36% (22.6us every 62.5us)
PDM Processing ISR
PDM ISR CPU Utilization
High = PDM ISR active
Cursor Delta = Sampling Rate
High = PDM ISR active
Cursor Delta = ISR CPU Utilization

## Slide 7: Power Consumption*
  *The current consumption described here is only for PMD processing and it DOESN’T include BLE interface, ADPCM and DC Filter current
PDM Processing Current Waveform
PDM Average Current Calculator
Two AAA 1250mAh Batteries
PDM System Battery Life
PDM Processing Stage | Pulse Current (uA) | Pulse Duration (us) | Total Duration (us) | Average Current (uA)
PDM Mic CPU Filtering | 6320 | 7.7 | 62.5 | 778.624
PDM Mic Hardware Filtering | 4880 | 54.8 | 62.5 | 4278.784
Total PDM Average Active Current |  |  |  | 5057.408
PDM Usage Modes | Average Current (uA) | Duration/ Day (mins) | Total Mins/Day (mins) | Average Current (uA)2
PDM Active Mode | 5057.4 | 20 | 1440 | 70.24167
PDM Inactive Mode | 1.3 | 1420 | 1440 | 1.281944
 | Total PDM Current |  |  | 71.52361
 | Battery Capacity (mAh) |  |  | 1250
 | Battery Life (days) |  |  | 728
Sleep Current = 4.88mA (Cursor delta)
PDM Processing Current = 6.32mA